## Slide 1: Regenerative SDR for NOAA Satellite Reception
Project proposal - Suryasaradhi

## Slide 2: Problem Statement
Reception of live NOAA satellite weather signal with minimum power consumption no internet
Expensive components to downconvert high frequency signals
Creation of a low-cost SDR with minimal components
  No mixer
  No Separate filter
  No separate amplification stage

## Slide 3: Approach
Fine and coarse control through quench and frequency control
Opamp adjustable gain stage
CB amp attenuator for Isolation
Use direct sampling

## Slide 4: Implementation
Build helical antenna – 135-140 Mhz, 50 ohms
  Test antenna – VNA (NanoVNA)
  Confirm VSWR less than 3 for the band
Satellite | Frequency (MHz) | Notes
NOAA-15 | 137.620 | Active
NOAA-18 | 137.9125 | Active
NOAA-19 | 137.100 | Active
NOAA-14 | 137.620 | Decommissioned
NOAA-17 | 137.500 | Decommissioned

## Slide 5: Implementation
Implement regenerative SDR in hardware – Simulation is close to impossible
Explore Super regeneration
Tested design
Unverified Super Regen

## Slide 6: Software
Implement GNU radio interface
  Implement streamer for gnu radio
  Create math blocks for doing operations on the received data
  Create flowgraph
  Implement quench clear control
Microcontroller
  STM32F4 (No FPGA – Overcomplicated)
  Target Sampling Rate: 3Mhz (1Mhz Nyquist’s Bandwidth)

## Slide 7: Results
Realised SDR
Less than 10mw power consumption for hardware
A mini portable weather station
Analysed frequency response of a regenerative reciever